PORT USAGE IN THE AG ENVIRONMENT

All AG node hosts

Receive:

SSH (TCP/UDP 22)

from each other and internal network

AG Beacon server (HTTP TCP 9999)  ***

from beaconserver.accessgrid.org 140.221.9.160

ESnet Beacon server (HTTP TCP 9999)  ***

from thorn.es.net 198.128.1.27

AG Beacon client (Multicast UDP 56464)  ***

from any to 233.2.171.1

ESnet Beacon client (Multicast UDP 47777)  ***

from any to 233.4.171.1

NTP (TCP/UDP 123)

from time server

Send:

SSH (TCP/UDP 22)

to each other

AG Beacon client (Multicast UDP/IGMP 56464)  ***  !!!!

to 233.2.171.1

ESnet Beacon client (Multicast UDP/IGMP 47777)  ***  !!!!

to 233.4.171.1

AG Beacon client (UDP 9997)  ***  !!!!

to beaconserver.accessgrid.org 140.221.9.160

ESnet Beacon client (UDP 9997)  ***  !!!!

to thorn.es.net 198.128.1.27

NTP (TCP/UDP 123)

to time server

Display Machine, aka DPPT|RPPT|VNC Client

Receive:

Video Conference (VIC) (Multicast UDP >= 50000)

[see attached list for addresses of each virtual venue]

from any to any multicast group

Web browser (HTTP TCP 80)

from anywhere

MUD (TCP 7777)

from venues.accessgrid.org 140.221.10.85

VNC (TCP 5800-5805,5900-5905)

[5800|5900 + X-windows screen number]

from server machine

Distributed PowerPoint (DPPT) (TCP 80, 5001)

from DPPT server machine

Remote PowerPoint (RPPT) (TCP ?? > 15000 recommended)

from RPPT server machine

Send:

MUD (TCP 7777)

to venues.accessgrid.org 140.221.10.85

Video Machine

Receive:

Video Conference (VIC) (Multicast UDP >= 50000)

[see attached list for addresses of each virtual venue]

from any multicast group

Send:

Video Conference (VIC) (Multicast UDP >= 50000)

[see attached list for addresses of each virtual venue]

to any multicast group

Audio Machine

Receive:

Robust Audio Tool (RAT) (Multicast UDP >= 50000)

[see attached list for addresses of each virtual venue]

from any multicast group

Send:

Robust Audio Tool (RAT) (Multicast UDP >= 50000)

[see attached list for addresses of each virtual venue]

to any multicast group

DPPT Server Machine

Receive:

DPPT control input (Multicast ???)

from DPPT Master(s)

Send:

DPPT control output (Multicast ???)

to DPPT Client(s)

DPPT Master Machine

Send:

DPPT control output (Multicast ???)

to DPPT Server

RPPT Server Machine

Receive:

RPPT control input (Multicast ???)

from RPPT Master(s)

Send:

RPPT control output (Multicast ???)

to RPPT Client(s)

RPPT Master Machine

Send:

RPPT control output (Multicast ???)

to RPPT Server

Bridges and Reflectors

Anyone know  ??

Virtual Venue Information

see: http://agschedule.ncsa.uiuc.edu/venues.asp

Key to editors:

??	Anyone care to fill in this section?

***	Doesn’t this actually apply to machines on which a beacon is started up,

not all AG node machines?

!!!!	I suspect some of these ‘clients’ should be servers.

data from Andrew Shewmaker

formatting and bits on RPPT by Chris Osland